Elimination Of Carbon from Smoke Level Indicator In Vehicle

Synopsis:

Introduction

Mechanical engineering without production and manufacturing is meaningless and inseparable. Production and manufacturing process deals with conversion of raw materials inputs to finished products as per required dimensions specifications and efficiently using recent technology

Objective& scope

Unlike the above conventional methods, our “CARBON LEVEL INDICATOR IN VEHICLE” is an easily installable, economically viable of vehicle security system.

Working

Carbon Level detection in the Vehicle can be sensed with help of Microcontroller.

This project is intended for use as a preventive device. A carbon Level-sensing element, which is a tin oxide (Sno2) semiconductor, which has low conductivity, increases depending on the carbon concentration in the vehicle.	The signal from the sensor is sensed with the reference voltage set in the A/D converter and the output triggers the Microcontroller constructed in Automatic sensing mode.

So that the buzzer is made to operate since the Controller circuit operates it. At the time Carbon Level is high. This high level is display in the Liquid Crystal Display unit.

Block Diagram:

Carbon

Neutralizer

Expected outcome

Carbon level is detected make it as neutral by chemical reaction

# Text boxes

POWER SUPPLY

MICRO CONTROLLER

CARBON

SENSOR

ALARM

RELAY

A/D CONVETER

LCD DISPLY