LOW COST HARVESTER MACHINE

SYNOPSIS

The low cost harvester machine is a machine that harvests grain crops. The name derives from the fact that it combines three separate operations, reaping, threshing, and winnowing, into a single process. Among the crops harvested with a combine are wheat, oats, rye, barley, corn (maize), soybeans and flax (linseed). The waste straw left behind on the field is the remaining dried stems and leaves of the crop with limited nutrients which is either chopped and spread on the field or baled for feed and bedding for livestock.

The low cost harvesters are one of the most economically important labor saving inventions, enabling a small fraction of the population to be engaged in agriculture.

INTRODUCTION

The low cost harvester was invented in the United States by Hiram Moore in 1834, and early versions were pulled by horse or mule teams. In 1835, Moore built a full-scale version and by 1839, over 50 acres of crops were harvested. By 1860, combine harvesters with a cutting width of several meters were used on American farms. In 1882, the Australian Hugh Victor McKay had a similar idea and developed the first commercial combine harvester in 1885, the Sunshine Harvester.

Combines, some of them quite large, were drawn by mule or horse teams and used a bull wheel to provide power. Later, steam power was used, and George Stockton Berry integrated the combine with a steam engine using straw to heat the boiler. Tractor-drawn, PTO-powered combines were then used for a time. These combines used a shaker to separate the grain from the chaff and straw-walkers (grates with small teeth on an eccentric shaft) to eject the straw while retaining the grain. Tractor drawn combines evolved to have separate gas or diesel engines to power the grain separation.

In 1911, the Holt Manufacturing Company of California produced a self-propelled harvester. In Australia in 1923, the patented Sunshine Auto Header was one of the first center-feeding self-propelled harvesters. In 1923 in Kansas, the Curtis brothers and their Gleaner Manufacturing Company patented a self-propelled harvester which included several other modern improvements in grain handling. Both the Gleaner and the Sunshine used Ford son engines. In 1929 Alfredo Rotarian of Argentina patented a self-propelled harvester. In 1937, the Australian-born Thomas Carroll, working for Massey-Harris in Canada, perfected a self-propelled model and in 1940 a lighter-weight model began to be marketed widely by the company. In 1952 Clays’ launched the first self- propelled combine harvester in Europe; in 1953, the European manufacturer CLAAS developed a self-propelled combine harvester named 'Herkules', it could harvest up to 5 tons of wheat a day. This newer kind of combine is still in use and is powered by diesel or gasoline engines. Until the self-cleaning rotary screen was invented in the mid-1960s combine engines suffered from overheating as the chaff spewed out when harvesting small grains would clog radiators, blocking the airflow needed for cooling.

A significant advance in the design of combines was the rotary design. The grain is initially stripped from the stalk by passing along a helical rotor instead of passing between rasp bars on the outside of a cylinder and a concave. Rotary combines were first introduced by Sperry-New Holland in 1975.

In about the 1980s on-board electronics were introduced to measure threshing efficiency. This new instrumentation allowed operators to get better grain yields by optimizing ground speed and other operating parameters.

WORKING PRINCIPLE

First, the header, described above, cuts the crop and feeds it into the threshing cylinder. This consists of a series of horizontal rasp bars fixed across the path of the crop and in the shape of a quarter cylinders. Moving rasp bars or rub bars pull the crop through concaved grates that separate the grain and chaff from the straw. The grain heads fall through the fixed concaves. What happens next is dependent on the type of combine in question. In most modern low cost harvesting augers, set parallel or semi-parallel to the rotor on axial mounted rotors and perpendicular to the cylinder on conventional (or perpendicular to the cross mounted rotor of Gleaner brand "Natural Flow" combines.) In older Gleaner machines, these augers were not present. These combines are unique in that the cylinder and concave is set inside feeder house instead of in the machine directly behind the feeder house. Consequently, the material was moved by a "raddled chain" from underneath the concave to the walkers. The clean grain fell between the raddled and the walkers onto the shoe, while the straw, being longer and lighter, floated across onto the walkers to be expelled. On most other older machines, the cylinder was placed higher and farther back in the machine, and the grain moved to the shoe by falling down a "clean grain pan", and the straw "floated" across the concaves to the back of the walkers.

APPLICATIONS

- Application of Agricultural purpose for low cost harvesting machine.

ADVANTAGES

- Simple in construction

- it can be transferred easily from one place to other place

- Maintenance cost is low

- Reduce the manpower

- Reduce the time of harvesting