AUTOMATIC SIDE STAND WITH BREAK LOCKING SYSTEM

Block Diagram:

Block Diagram:

This system aims to leave the side stand and Brake locking for vehicle automatically when the engine starts.  The block diagram consists of an Engine start sensor circuit, a timer, relay, motors, Side stand mechanism and Brake locking mechanism.

The engine starts sensor circuit to sense the engine start and is working as logic circuit.  It compares the input, which is obtained during the engine start and produces output to relay driver circuit.

Relay driver is used drive the relay.  The relay is control to the motors and the motors are control for side stand mechanism and Brake Locking Mechanism.  Then the side stands and Brake locking operation are performed foe automatically.  The ‘ON’ time of motor is set in the timer circuit.  Thus the sides stand and brake-locking system can be leaved for automatically.

# Text boxes

Brake Lock

Mechanism

# DC

MOITOR

RELAY DRIVER & RELAY

TIMER CIRCUIT

ENGINE START SENSOR

Side stand

Mechanism

# DC

MOITOR