HYDRAULIC BREAK SHOW RIVETING MACHINE

SNAPSIS

When considering industrial machinery, the hydraulic riveting machine is the perfect machine shop tool for the riveting industries. Our riveting machine consists of a Hydraulic Jack, screw rod, ram and frame stand.

This is a hand operated one. The Hydraulic Jack consists of piston, piston rod, hydraulic oil and screw rod. The handle is used to pushing the hydraulic piston upwards. The brake show is fixed at the end of the Hydraulic Jack. The pressurized oil pusses the Hydraulic Jack piston forward due to oil pressure. Already the rivet is fixed at the top of the brake show. The screw rod is fixed at the top of the frame stand. The ram is fixes to this screw rod. The ram is striking the rivet forcely, due to the movement of the hydraulic piston.

# INTRODUCTION

The hydraulic press is one of the most flexible machines on the market, allowing the fabricator or ironworker to shear, punch, bend, scroll, and press thousands of different parts. When considering industrial machinery, the hydraulic riveting press is the perfect machine shop tool for the metal fabricator.

The hydraulic riveting press fits any small to medium-sized industry when machinery for large-scale production must necessarily make way for machinery with distinctly lower production costs. The operating procedure of hydraulic riveting machine is simple when compared to other riveting machine. Biggest improvements were placing the Hydraulic Jack near the ram. The hydraulic riveting press is most strength due to less deflection in the table.

## WORKING OPERATION

Hydraulic jack consists of piston, piston rod, screw rod and hydraulic oil. The hydraulic jack reciprocating handle is move upward and downward continuously, so that the compressed oil goes to the hydraulic jack piston.

The end of the piston rod the break show is fixed. The compressed oil pushes the hydraulic jack piston forward. Already the rivet tool is fixed in between break show and screw rod ram. The different size of the break show is riveted by adjusting the screw rod arrangement. The break show is riveted by pumping the hydraulic jack piston upwards and the break show rivet is strike the screw rod ram.

ADVANTAGES

- Hydraulic Riveting machine develops greater forces than mechanical pressure and hence it is for forming, bending, riveting and drawing and extrusion operations.

- The hydraulic riveting machine can exert its full forces at any position of the ram stroke whereas the force is maximum at the end of stroke in mechanical press.

- The sliding action of the rivet slide is uniform.

- The length of stroke can be varied even within small ranges.

- No noise, no vibrations and hence smooth operation.

- Stroke length and position of stroke can be varied easily.

- Wide speed ranges.

- Inertia losses are less.

## DISADVANTAGES

- Initial cost is high.

- High maintenance cost.

APPLICATION

- The hydraulic riveting  machine  brakes can be fitted with hundreds of tooling options for acting as a press brake (using the table as the level for accuracy),

- Ram bender (for pipe or solids),

- Rotary draw tubing bender

- Shear, punch, ornamental iron twisting machine, straightener, etc.

- This machine tool is great for any welding shop, fabricator, or general job shop.