FABRICATION OF MECHANICAL CAN CRUSHER

ABSTRACT

Introduction

Mechanical engineering without production and manufacturing is meaningless and inseparable. Production and manufacturing process deals with conversion of raw materials inputs to finished products as per required dimensions specifications and efficiently using recent technology

Objective& scope

Can crusher is used to crush the can in very high speed, it more suitable for plastic re usable industries ,in these industries the crushed can are dumped in a heavy mask and send to the furnace for melting so this crushing process is carried in this machine which is fabricated by our self

Working principle

The total structure is made of mild steel frames in which all the parts are assembled over it. the machine consist of crank shaft, connecting rod ,slider block, plumer block, motor ,male die and female, when a motor is switched ON the power is transmitted from motor to crank shaft via belt , so when crank shaft rotates the connecting rod will up and down and crushes the can automatically.

Advantage

- It reduces the burden of the worker

- It is easy to operate

- stock length is adjustable

Disadvantage

1) It is used for mass crushing only

2) Runs at constant speed

# Text boxes

ECWAY TECHNOLOGIES

IEEE PROJECTS & SOFTWARE DEVELOPMENTS

OUR OFFICES @ CHENNAI / TRICHY / KARUR / ERODE / MADURAI / SALEM / COIMBATORE

BANGALORE / HYDRABAD

CELL: +91 98949 17187, +91 875487 1111 / 2111 / 3111 / 4111 / 5111 / 6111 / 8111

VISIT: www.ecwaytechnologies.com | www.ecwayprojects.com

Mail to: ecwaytechnologies@gmail.com | ecwayembedded@gmail.com