FIRE PROTECTIVE ANG GOVERNING SYSTEM BY AUTOMATION IN INDUSTRIES

SYNOPSIS

In most cities, firefighters are trained members of government-supported organizations, such as fire departments. Elsewhere, fire-fighting organizations are primarily composed of volunteers, or “vols.” Fire-fighting organizations also help design and implement fire-prevention programs, which may include such measures as building codes requiring fire alarms, regularly located fire-extinguishing equipment, internal fire walls to help contain a fire, sprinkler systems, the use of fire-retardant construction materials, and safe electrical wiring. Educating the public about fire safety and fire-prevention practices is an important part of all fire-prevention programs.There is many fields in which artificial intelligence (AI) may be related to electrical, mechanical lingistres, psychology and philosophy.  We use this concept in a simpler application of fire detection.  In our project, we use a sensor to detect fire, which sends the information to a micro-controller, which is written with a program based on assembly language, which turns nozzle head of the fire fighter to that direction.

Two-DC motors are provided.  One for the up and down movement and another one for the clockwise and anticlockwise rotation.  A valve opens in the nozzle, which is controlled by the same. Hence we have chosen this as criteria to design a machine to perform fire protective operation for smaller area.

Merits:

- The intelligence of the fire fighter can detect fire for about one feet square area.

- The range of detection of fire is 360º, in all directions.

- The nozzle adjustments are such that water or any chemicals, which are used to extinguish fire, can be used here.

- Since the project is based on the Micro controller, it is compact and swift and response.

No external devices are used here to control